## Slide 1: A Yang Data Model for ACTN VN Operation draft-lee-teas-actn-vn-yang-12
Young Lee, Dhruv Dhody, Igor Bryskin | Huawei
Daniele Ceccarelli | Ericsson
Bin Yeong Yoon | ETRI
Haomian, Xian, Sergio, Qin, Takuya, Peter | Contributors

## Slide 2: Introduction
A YANG data model for the ACTN Virtual Network Service (VNS) operation that is going to be implemented for CMI (between CNC and MDSC).
  Aligned to Customer Service Model
  VN Instantiation, VN Computation, VN Lifecycle
  Access Points (AP) and Virtual Network Access Points (VNAP)
  Virtual Network (VN)
    List of VN members
  Other VN Operations
    Multi-src/Multi-dest
  As per the ACTN Informational Model

## Slide 3: Major Change
Coupling with the TE Topology Yang Model
  Removed any duplicated information that can be found in TE Topology
    Constraints
    Explicit Path
    Underlay path
    Etc.
Simplification of model for both VN Type 1 & VN Type 2
JSON examples are added
Access
AP/ VNAP
LTP
Customer’s Virtual Network
VN
Abstract Node
Customer Site to Site connection
VN-Member
Entry in the connectivity matrix of the abstract node
TE Topology
ACTN VN

## Slide 4: Overview
ACTN VN Yang Model
AP/VNAP
VN
VN-Member
Abstract Topology with a
Single Node
Underlay
For both VN Type 1 or Type 2 VN Yang model rely on a single node in the abstract TE Topology
The abstract node has
  connectivity-matrices
  connectivity-matrix [id]
  The attributes directly under container connectivity-matrices are the default attributes for all connectivity-matrix entries when the per entry corresponding attribute is not specified. When a per entry attribute is specified, it overrides the corresponding attribute directly under the container connectivity-matrices.
Connectivity
Matrix

## Slide 5
ACTN VN
AP
VNAP
VN
VN-Member
From
Constraints?
Policy?
To
Node
connectivity-matrices
underlay
primary-path
path-constraints
Optimizations
computed-path-properties
connectivity-matrix [id]
From
underlay
Primary-path
path-constraints
Optimizations
To
tunnel-termination-points
tunnel
/nw:networks/nw:network/nw:node/te-node-id
global
Per entry
Overview

## Slide 6: How: Reference to TE Topology Yang Model
Access | AP/ VNAP -> LTP Ltp of type te-types:te-tp-id
Customer’s Virtual Network | VN -> Abstract Node vn-topology-id of type te-types:te-topology-id abstract-node -> /nw:networks/network/node/tet:te-node-id (reference)
Customer Site to Site connection | VN-Member -> Entry in the connectivity matrix of the abstract node connectivity-matrix-id -> /nw:networks/network/node/tet:te/te- node-attributes/connectivity-matrices/connectivity-matrix/id (reference)
All parameters which are can be set as global attributes to VN are set in the connectivity-matrices (such as bandwidth) and an attribute for a particular VN-member is set in the connectivity-matrix [id] (such as explicit path)!
Duplicate parameters in ACTN VN Yang model are removed!

## Slide 7: VN Type 1
VN 1
  VN-Member 1 L1-L4
  VN-Member 2 L1-L7
  VN-Member 3 L2-L4
  VN-Member 4 L3-L8
  This VN has following properties
    Bandwidth 500
    Optimize by delay
Abstract Topology with a
Single Node
14: L1-L4 | 17: L1-L7
24: L2-L4 | 38: L3-L8
Connectivity
Matrix
Attributes
  connectivity-matrices
  These properties
  are set in TE Topo
VN is seen as edge to edge links (VN-members) setup as tunnels across underlying networks!

## Slide 8: VN Type 2
VN is seems as a topology of virtual nodes and links
To ease mapping between VN Yang Model and TE models, an abstract single node topology is created with VN topology as the underlay!
The same mapping as VN Type 1 is reused.
VN 2
  VN-Member 1: L1-L8 via S3, S67110, S11
    Set via the underlay path in connectivity-matrix[id]
S3
S9
S124
S67110
S5
S8
S11
Abstract Topology with a
Single Node
VN Topology
Underlay
Underlay

## Slide 9: Role of ACTN VN Model
Customer view of VN
Innovative Services
Service Mapping
AP / VNAP
VN Compute
Multi-Src / Multi-Dest
VN as a single entity (as per the ACTN info model)
~ Service Model

## Slide 10: ACTN VN Yang Tree
module: ietf-actn-vn
+--rw actn
+--rw ap
| +--rw access-point-list* [access-point-id]
| +--rw access-point-id uint32
| +--rw access-point-name? string
| +--rw max-bandwidth? te-types:te-bandwidth
| +--rw avl-bandwidth? te-types:te-bandwidth
| +--rw vn-ap* [vn-ap-id]
| +--rw vn-ap-id uint32
| +--rw vn? -> /actn/vn/vn-list/vn-id
| +--rw abstract-node? -> /nw:networks/network/node/tet:te-node-id
| +--rw ltp? te-types:te-tp-id
+--rw vn
+--rw vn-list* [vn-id]
+--rw vn-id uint32
+--rw vn-name? string
+--rw vn-topology-id? te-types:te-topology-id
+--rw abstract-node? -> /nw:networks/network/node/tet:te-node-id
+--rw vn-member-list* [vn-member-id]
| +--rw vn-member-id uint32
| +--rw src
| | +--rw src? -> /actn/ap/access-point-list/access-point-id
| | +--rw src-vn-ap-id? -> /actn/ap/access-point-list/vn-ap/vn-ap-id
| | +--rw multi-src? boolean {multi-src-dest}?
| +--rw dest
| | +--rw dest? -> /actn/ap/access-point-list/access-point-id
| | +--rw dest-vn-ap-id? -> /actn/ap/access-point-list/vn-ap/vn-ap-id
| | +--rw multi-dest? boolean {multi-src-dest}?
| +--rw connetivity-matrix-id? -> /nw:networks/network/node/tet:te/te-node-attributes/connectivity-matrices/connectivity-matrix/id
| +--ro oper-status? identityref
+--ro if-selected? boolean {multi-src-dest}?
+--rw admin-status? identityref
+--ro oper-status? identityref
+--rw vn-level-diversity? vn-disjointness

## Slide 11: Next Step
This update of draft is based on feedback received during the last IETF to reuse existing TE yang model as much as possible.
This update does just that and works well with abstract TE topology model
Request for WG Adoption!

## Slide 12
Thank You!

## Slide 13: Backup Slides

## Slide 14: Typical Interactions: VN Type 1
CNC
MDSC
Set Attributes, Connectivity Matrix, via Single Node Abstract TE Topology
POST /nw:networks/nw:network/nw:node/te-node-id/tet:connectivity-matrices/tet:connectivity-matrix
200 OK
Create VN with VN members, VNAP and map it to the TE Topology model
POST /actn/vn/vn-list/vn-id
200 OK
Get VN Status, selected VN-members in case of multi-src/multi-dest
GET /actn/vn/vn-list/vn-id

## Slide 15: Typical Interactions: VN Type 2
CNC
MDSC
Set Attributes, Connectivity Matrix, via Single Node Abstract TE Topology
Explicitly creating a single node topology
POST /nw:networks/nw:network/nw:node/te-node-id/tet:connectivity-matrices/tet:connectivity-matrix
200 OK
Create VN with VN members, VNAP and map it to the TE Topology model
POST /actn/vn/vn-list/vn-id
200 OK
Get VN Status, selected VN-members in case of multi-src/multi-dest
GET /actn/vn/vn-list/vn-id
The CNC creates a single node topology by itself, in this way VN Type 1 and VN Type 2 would have similar interactions

## Slide 16: Typical Interactions: VN Type 2
CNC
MDSC
Set any changes in attributes, Connectivity Matrix, via Single Node Abstract TE Topology
POST /nw:networks/nw:network/nw:node/te-node-id/tet:connectivity-matrices/tet:connectivity-matrix
Create VN with VN members, VNAP first
POST /actn/vn/vn-list/vn-id
200 OK
Get VN Status and information related to the single node abstract topology and mapping
GET /actn/vn/vn-list/vn-id
The MDSC creates a single node topology by itself and maps it to the ACTN VN Yang model. Any attribute changes are done next via the te topology model
MDSC populates a single node abstract node topology by itself
200 OK

## Slide 17: Multi-Src / Multi-Dest
Multiple VN members are configured and marked with multi-src or multi-dest option
The MDSC selects the VN member to actually setup and create a connectivity matrix entry in the single node abstract topology based on the selected.
MDSC is free to change the selected VN-member in coordination with CNC
VN-Member 1 | L1-L4(*)
VN-Member 2 (selected) | L1-L7(*)
VN-Member 3 | L2(*)-L4
VN-Member 4 (selected) | L3(*)-L4
(*) | Multi-src or Multi-destination enabled