## Slide 1: Hierarchy of IP Controllers (HIC) draft-li-teas-hierarchy-ip-controllers-00
Zhenbin Li, Dhruv Dhody, Huaimo Chen - Huawei

## Slide 2: Introduction
This I-D describes how multiple IP controllers work in a hierarchical fashion
  How the ACTN framework is applied to IP controllers
  Interactions between TE and non-TE components
  Control Plane and Management Plane considerations
IP Services Realization
  Seamless MPLS
  L3VPN
  L2VPN/EVPN
Scope for possible new extensions
Introduction
Key Concepts
Protocols and Models
Services
Future

## Slide 3: Hierarchy of IP controllers (HIC)
The Super Controller receives request from the network/service orchestrator to setup dynamic services spanning multiple domains.
The Super Controller breaks down and assigns tasks to the domain controllers, responsible for communicating to network devices in the domain. It further coordinates between the controller to provide a unified view of the multi-domain network.
Super Controller
Domain
Controller
Introduction
Key Concepts
Protocols and Models
Services
Future

## Slide 4: Mapping to ACTN
Main Functions in ACTN
Multi-domain Coordination
Customer mapping/translation
Virtualization/Abstraction
Virtual Service Coordination
Domain Controller
Super Controller
MDSC
PNC
Other non-TE interactions
MPI
Interface b/w controllers
  TE & non-TE
  Control Plane Protocol
    PCEP, BGP
  Management Protocol
    RESTCONF/NETCONF/gRPC
Child PCE
Parent PCE
Introduction
Key Concepts
Protocols and Models
Services
Future

## Slide 5: Topology
Domain Controller / PNC
Learn Domain Topology
IGP, BGP-LS, PCEP-LS, Yang based
Super Controller / MDSC
Learn abstract topology from Domain Controller
Level of abstraction
BGP-LS , PCEP-LS, Yang based interface
Manage E2E topology
Introduction
Key Concepts
Protocols and Models
Services
Future

## Slide 6: Path Compute/Instantiate
Domain Controller computes/setup per-domain paths
Super Controller responsible for E2E inter-domain paths
PCEP Based
  Stateful H-PCE framework on how E2E path computation, setup, stitching etc
YANG Based
  Path Computation Yang Model (via RPC)
  TE Tunnel Yang Model
Same as ACTN framework!
Introduction
Key Concepts
Protocols and Models
Services
Future

## Slide 7: Seamless MPLS
IGP-X1 (MBH) | IGP-Y (Core) | IGP-X2 (MBH)
Super Controller
E2E BGP LSP
Per Domain LSP
Extend MPLS to the edge mobile backhaul.
The super controller is aware of the E2E topology
Super Controller is responsible to setup the seamless MPLS service from the service model
The super controller selects the right ABR and create corresponding per-domain tunnels
Based on the service model, the Super Controller translates to the network configuration model for the domain controller.
The domain controller further breaks into the device configuration model to the PE/ABR to make E2E services.
Routes can also be learned via the BGP sessions between Domain Controller and Super Controller for intelligent decisions
Domain
Controller
Introduction
Key Concepts
Protocols and Models
Services
Future

## Slide 8: L3VPN
The Super-controller implements the L3SM model and translate it to network models towards the domain controller, which in turn translate it to the device model.
Based on QoS/Policy, the Super Controller may -
  Set the tunnel selection policy at the PE/ASBR routers so that they could select the existing tunnels
  Select an existing tunnels at the controller level and bind it to the VPN service
  Initiate the process of creating a new tunnel based on the QoS requirement and bind it the VPN service
  Initiate the process of creating a new tunnel based on the policy
Apart from Management Plane, control plane interface between controllers can also be used to setup and maintain the L3VPN service!
Super Controller
L3SM
* -- applicable to L2VPN/EVPN in similar fashion!
Domain
Controller
Introduction
Key Concepts
Protocols and Models
Services
Future

## Slide 9: PCE / PCEP
PCE
Stateful PCE
PCE Initiation
Stateful H-PCE
Applicability to ACTN
H-PCE and other inter-domain procedures
PCE / PCEP well positioned to meet the requirements for HIC / ACTN!
Introduction
Key Concepts
Protocols and Models
Services
Future

## Slide 10: YANG Models
Service Models (L3SM, L2SM)
Network Configuration Models (?)
Device Configuration Models
OAM
Topology Related
Tunnel related
VN and Service-Mapping related
?
Introduction
Key Concepts
Protocols and Models
Services
Future

## Slide 11: Possible Features/Extensions
Initial Configurations between controllers
Relationship / Role of controllers
Learning the mutual capabilities of controllers
Handling of multiple instances of controller for reliability
?
Service Discovery (DNS)
Discovery via other protocols
Initial Session Establishments
Introduction
Key Concepts
Protocols and Models
Services
Future

## Slide 12: Next Steps
Get Feedback
  What is missing?
  What else can be added / removed?
  Is such an informational document useful?
Identified Gaps
  Need to add more details about other Yang Models that are useful between controllers
  Need to add more details about usage of BGP between controllers
  Need to add more details about OAM
  If you have expertise in these areas please provide help – Call for collaboration!
Introduction
Key Concepts
Protocols and Models
Services
Future

## Slide 13: Thank you!